## Slide 1
Persistent Processor Architecture
Jianping Zeng, Jungi Jeong*, Changhee Jung
* Now at Google
Purdue University
Notes: Good afternoon, everyone. I will be presenting our paper PPA: Persistent Processor Architecture for whole system persistence.

## Slide 2
Prevalence of Nonvolatile Memory (NVM)
High areal density
Comparable speed as DRAM
Byte-addressability with load/store
Nonvolatility (data persistence)
Notes: As you know, nonvolatile memory (NVM) has been commercialized by many vendors, such as [click] Intel PMEM, [click] Samsung memory semantic SSD, [click] Everspin STT-MRAM, and [click] Fujitsu ReRAM. They can be deployed in data centers to achieve high performance thanks to the unique benefits such as [click] high areal density [click] comparable speed as DRAM, byte-addressability with store/load instructions, and nonvolatility [click]
To better utilize the benefits of NVM [click]

## Slide 3
NVM
Persistent Heap
Reg. File
Caches
DRAM Cache
NVM
Main Memory
Memory Mode
Reg. File
Caches
DRAM Main Memory
App-Direct Mode
Intel PMEM’s Two Operation Modes
Transparence and
High Performance
Persistence but No Transparence and High Performance
Persistent
Programming
is hard
PMEM is not
persistent?
Notes: Intel PMEM provides two use modes; [click] memory mode and [click] app-direct mode.
When PMEM is used under memory mode, DRAM works as a last-level cache, while PMEM is used as a main memory, which is [click] transparent to user program. Thanks to the high areal density, [click] program sees a huge memory space and achieves high performance. However, [click] data in NVM are dead when power failure happens. Ironically, [click] Persistent memory is not persistent at all!
On the other hand, in the app-direct mode, [click] data in NVM are durable and persistent. But [click] this mode is not transparent, meaning that we need to modify program source code, [click] leading to programming burden.
As a result, both two modes do not fully utilize the potential of NVM technologies.
Then, there is a natural question coming up, can we have both large memory space and non-volatility with transparency guaranteed? Yes, WSP can do that; let’s see how that is possible.

## Slide 4
ARF
Caches
NVM Main Memory
WSP: Unlocking the Full Potential of NVM
DRAM Cache
* WSP: Whole-System Persistence
Memory Mode
* ARF: architectural register file
Notes: With PMEM memory mode, we already achieve [click] high performance with dram as a cache and [click] transparency. Our goal is to equip the entire system with persistence. To achieve that, [click] we extend the persistence domain all the way up to register file including caches along the way. [click] This is so-called whole system persistence. In particular, whole system persistence requires correct recovery across power failure, which is so-called crash consistency.

## Slide 5: Logging-Based Crash Consistency Is Super Expensive
ARF
L1
NVM Main Memory
DRAM Cache
L2
L3
* ARF: architectural register file
High overhead (2x-4x) with prior logging techniques [Atlas;OOPSLA’14] [Nvthreads; EuroSys’17] [JustDO; ASPLOS’16] [iDO; MICRO’18]
Need to pay for such high persist barrier overhead no matter which logging is used
Notes: To achieve crash consistency, [click] prior approaches usually leverage logging involving expensive persist barriers [click] to flush the data being stored all the way down to NVM and [click] wait for their acknowledgements on the way back. [click] Therefore, no matter which logging technique is used, users have to pay for such high persist barrier overhead periodically. Fortunately, we found out our prior work ReplayCache has a potential to achieve high performance crash consistency.

## Slide 6: ReplayCache [MICRO’21] with Roll Forward Recovery
ARF
L1
NVM Main Memory
DRAM Cache
L2
L3
* ARF: architectural register file
Program resumption from power failure point
Just-in time (JIT) checkpoint ARF to NVM upon power failure
Only do just-in-time checkpointing upon power failure
Notes: [click] ReplayCache relies on a so-called roll forward recovery that can resume program execution exactly from power failure point. To achieve that, [click] upon impending power failure, [click] this technique just in time checkpoints entire architectural registers to NVM. [click] Once power comes back, [click] it restores architectural registers and [click] resumes program execution from the failure point. [click] The beauty of this approach is that it only does just in time checkpointing at the moment of power failure, meaning that, when program is running, there is no overhead at all compared to prior logging approaches.
However, in the presence of volatile caches, just in time checkpointing architectural registers along is not enough to ensure crash consistency. Let’s visit an example to see what is the fundamental reason for that. [click]

## Slide 7
Reason for Crash Inconsistency of Volatile Cache
…
Store r2, [r3]
…
r4 = Load [r3]
…
New
data
New
data
Power
interrupted
r2
r3
r3
ARF
DRAM Cache
L2
L3
* ARF: architectural register file
L1
Old
data
NVM Main
Memory
I am the evil
Notes: In this example, we assume the store and load access the same memory location. [click] When power is on, [click] processor executes the store instruction and writes its data to the L1D cache (we assume a cache hit here). [click] Then processor continues executing following load. [click] When a power failure happens at that load, [click] we detect that and just in time checkpoint entire architectural register file to NVM. [click] then all data in RF and Caches are lost when power is off. [click] Once power comes back, [click] RF content we once just in time checkpointed is now restored from NVM, [click] here, register r2 and r3 are restored, [click] Then we restart the program from the failure point. But [click] processor reads an old data instead of the new data just written by the store, [click] causing crash inconsistency issue. [click] We can see the crash inconsistency issue is caused by the store left behind the power failure. [click]

## Slide 8
…
Store r2, [r3]
…
r4 = Load [r3]
…
ReplayCache [MICRO’21]: Unpersisted Stores
Power
interrupted
* Recovery status after power failure happens
r2
r3
r3
ARF
DRAM Cache
L2
L3
L1
Old
data
NVM Main Memory
New
data
New
data
Notes: To deal with unpersisted stores, ReplayCache proposes to replay those stores before resuming from the failure point. Here, the figure shows the recovery status after power failure happens. [click] When power comes back, [click] RF data is restored from NVM, like register r2 and r3, as with original recovery protocol. [click] Then processor replays that problematic store again with recovered register r2 and r3 [click], ensuring the store is persisted. [click] processor then resumes at the power failure point to execute that load instruction [click] by loading the new data. [click] As a result, we correctly recover the program states.

## Slide 9
ReplayCache [MICRO’21] Incurs High Run-time Overhead Due to Its Software-Oriented Design.
Persistent Processor
Architecture (PPA) Can
Help!!
Notes: However, ReplayCache incurs too much performance overhead on server processors due to its software-oriented design. With that in mind, [click] we come up with high performance processor based whole system persistence, which we call PPA: persistent processor architecture. Before talking about how PPA works, let’s show you a few challenges PPA must deal with.

## Slide 10
Register Reuse Prevents Store Replaying
Compiler reuses store registers whenever it can.
Store integrity : register operands of stores must be not overwritten by following definitions.
…
Store r0, [10]
…
= r1 + 1
…
r0
Write-after-read
(WAR) dep
Power
interrupted
Notes: It is not always possible to replay stores [click] because compiler never expects replaying stores, their registers are likely to be reused by following definitions. As you can see here, [click] we have a write-after-read (WAR) dependence on store register r0. Because of the WAR dependence, [click] in the wake of power failure, [click] replaying the store will write an increased value into memory location, [click] leading to failed program recovery. To address this issue, [click] we come up with a new program property called store integrity. The idea is super simple. We just ensure that store registers should not be overwritten. The good news here is that current out of order cores already have an ability to eliminate such false register dependence.

## Slide 11
PPA Leverages Dynamic Register Renaming to Achieve Store Integrity
…
Store p0, [10]
…
= p1 + 1
…
p2
(b) Store integrity by renaming
r0
* Assume the store commits
…
Store r0, [10]
…
= r1 + 1
…
r0
Write-after-read
(WAR) dep
(a) Original assembly code
Dynamic register renaming
Notes: Let’s look at how it works. Assume the core already commits the store instruction. [click] with dynamic register renaming, [click] when the core pipeline tries to execute the addition instruction, [click] it will use physical register p2 to replace the architectural register r0 so that it can eliminate the WAR dependence on store register p0 and [click] ensure correct store replaying.
As you will see later, we should prevent those store registers such as p0 from being recycled. Because of that, you might think enforcing store integrity puts more pressure on physical register file, but it is not true. [click]

## Slide 12
Abundant Free Physical Registers in Out-of-Order Cores
CPU2006
CPU2017
# Free Physical
Registers
SPLASH3
115
99
99
122
103
127
101
112
116
WHISPER
120
110
STAMP
102
112
67
Integer (180)
Floating-Point (168)
All gmean
Mini-apps
* Numbers collected on a simulated Skylake core
Notes: [click] This is because we find that modern out-of-order cores have a lot of unused physical registers that can minimize the register pressure. As shown in the figure, an Intel Skylake out-of-order core has 115 free of 180 integer registers and 102 free of 168 floating-point registers.
But it does not mean physical register file never runs out. We must handle this structural hazard of the register file.

## Slide 13: Region-Level Persistence for Store Integrity
ST1: Store p0, [10]
ST2: Store p1, [20]
…
r3 = load [p2]
ST3: Store r3, [30]
ST1: Store p0, [10]
ST2: Store p1, [20]
…
r3 = load [p2]
ST3: Store r3, [30]
Rg2
Rg1
NVM Main Memory
ST1
ST2
No Store Integrity
* Omit caches for the sake of example
Notes: Let me walk you through an example to show how PPA handles this problem. [click] When power is on, [click] processor keeps executing following instructions. Here, [click] we assume the core pipeline runs out of physical registers at renaming stage, that indicates, from this point, [click] it is impossible to enforce store integrity anymore. To free the registers, [click] PPA persists prior stores to NVM. here the key insight is that we don’t have to keep the registers of the stores if they are already persisted. Once prior stores are all persisted, [click] we place a region boundary that serves as a natural recovery point in case the following region gets interrupted. [click] In this way, PPA allows each region to have freedom to reuse all physical registers for its execution.
Now, PPA achieves region-level persistence with store integrity enforced without worrying about the lack of free registers. But this requires PPA to wait for the completion of all prior stores at each region boundary. [click]

## Slide 14
Asynchronous Store Writeback to Reduce Region-Level Persistence Overhead
NVM
Cache
ST1
# Unpersisted
cachelines
0
1
L1D Cache Controller
0
ST1: Store p0, [10]
…
…
…
p0 = load [p2]
Store p0, [30]
ST1
Notes: To reduce such pipeline stalls, PPA persists the data being stored to NVM in the background. For this purpose, [click] PPA proposes a register to track the number of unpersisted stores of each region. Here, the register is initialized to 0. [click] each time once the data being stored is merged to L1D Cache, [click] we increase the register by 1. [click] While the cacheline is flushed, processor keeps executing in parallel. [click] Once ST1 arrives in NVM, the register is cleared. Whenever program control encounters a region boundary, it checks the register to see if it is zero. If so, [click] we can move on to the next region because it turns out all prior stores have already been persisted. Now, PPA works correctly to achieve high-performance region-level persistence, let’s see how PPA prepares processor architecture for power failure recovery with store integrity guaranteed [click]

## Slide 15: PPA Microarchitectural Diagram
Fetch
Decode
Out of Order Scheduling
Load/Store
Unit
Load Queue (LQ)
Store Queue (SQ)
Register Alias
Table (RAT)
Physical
Register File
Reorder Buffer (ROB)
MaskReg
Committed
Store Queue (CSQ)
PC
LCPC
Commit Rename Table (CRT)
Signal
Core
L1
NVM Main Memory
DRAM Cache
L2
L3
I$
D$
Store-to-load
forwarding
* LCPC: last committed program counter
Notes: This is the architectural diagram of PPA. [click] Here bold rounded boxes along with thick data paths are newly proposed by PPA, while [click] blue should be just-in-time checkpointed to NVM at the moment of power failure. Among them, [click] LCPC is used for failure recovery pointing to the last committed instruction before power failure. Note that we just in time checkpoint only a part of physical register file. Let’s go over the remaining structures one by one. [click]

## Slide 16
MaskReg for Store Integrity
Store p0, [10]
…
Add p1, p0, 1
MaskReg
Free List
Must prevent store registers from being reclaimed
MaskReg: tracks source registers of committed stores
* Assume 2 physical registers p0 and p1
p0
p0
p0
p1
p0
Store Integrity is broken!
Notes: As we all know, out of order cores would reclaim physical registers once it turns out they are no longer used. In this example, [click] once the core pipeline commits the addition instruction, [click] store register p0 is reclaimed back to the free list, [click] breaking store integrity. To address this issue, [click] PPA needs to prevent committed store registers from being reclaimed. For this purpose, [click] PPA proposes a vector register called MaskReg to track source physical registers of committed stores. [click] Here, in this example, [click] Once the store is committed, we [click] mark p0 in MaskReg. [click] When the core pipeline commits the addition instruction, the thing becomes different, [click] PPA does not reclaim p0 to the free list. In this way, [click] PPA ensures that store registers are never to be overwritten.

## Slide 17: What PPA Does Across Power Failure
Store integrity is ensured while power is on
Time
Notes: So far, we talk about how store integrity is guaranteed when program is running. For the rest of my talk, [click] I will explain what PPA does at the moment of power failure and [click] how to recover when power comes back.

## Slide 18
What PPA Just-In-Time Checkpoints
ST1: Store p0, [10]
ST2: Store p1, [20]
…
p0
[10]
p1
[20]
CSQ
Power
interrupted
LCPC
p0
p1
MaskReg
CRT
r0
p0
r1
p1
PRF
p0
p1
p2
p3
NVM Main Memory
CRT: Commit Rename Table
Notes: For crash consistency purpose, PPA has to just in time checkpoint 5 structures. [click] In addition to LCPC, [click] we should checkpoint CSQ that maintains metadata for committed stores for their replaying once power comes back. Since LCPC points to the store ST2, we have those two stores contained in CSQ. Note that CSQ only maintains the source physical register index, and this applies to CRT table and MaskReg. Also, [click] we need to checkpoint an existing hardware component, commit rename table that tracks mapping from architectural registers to physical registers of prior committed instructions. Although we don’t show the definitions of architectural registers r0 and r1 in this code, they are ensured to be committed. This is the reason why we have their mappings in CRT table. [click] PRF is kind of interesting, we consult CSQ and CRT to checkpoint only a part of physical registers such as p0 and p1 since other physical registers are not needed for store replaying and program resumption in the wake of power failure. [click] we also need to checkpoint MaskReg that is required for correct store integrity once power comes back. [click] When the power is about to be cut off, we just in time checkpoint all these 5 structures to NVM. So that they can be recovered in the wake of power failure. Now, let’s see PPA’s failure recovery protocol.

## Slide 19: What PPA Just-In-Time Restores
ST1: Store p0, [10]
ST2: Store p1, [20]
…
p0
[10]
p1
[20]
CSQ
Power
interrupted
LCPC
p0
p1
MaskReg
CRT
r0
p0
r1
p1
PRF
p0
p1
NVM Main Memory
ST1
ST2
Notes: Here, we see PPA’s architectural states across power failure. [click] In the wake of power failure, we restore those 5 structures. [click] With restored register p0 and p1 in mind, [click] we replay those two unpersisted stores. Thereafter, [click] we set PC to the instruction following the LCPC to continue program execution. In this way, PPA can achieve correct failure recovery. Now, let’s see the evaluation and resulting numbers [click]

## Slide 20
Gem5 Simulator
Benchmarks
Comparing Schemes
  Original program on PMEM’s memory mode
  The state-of-the-art WSP Capri [HPDC’22]
  PPA
Processor | 8-core, Out-of-Order, 2GHz, Skylake running on Ubuntu 18.04 FS mode
L1I & L1D | Private, 32/64KB, 8-way, 3/4-cycles, writeback
L2 Cache | Shared, 16MB, 16-way, 44-cycles, writeback
DRAM Cache | 4GB DDR4 2400 8x8, writeback
PMEM | 32GB, Read=175ns/Write=90ns, 16-entry WPQ, 2.3GB/s write bandwidth
CSQ | 40-entry FIFO queue
Methodology and Evaluation
CPU2006 | CPU2017 | SPLASH3 | WHISPER | STAMP | Mini-apps
Notes: We implement PPA on top of the gem5 simulator to model an 8-core Skylake processor with 2-level cache hierarchy. We also evaluate L3 cache for sensitivity analysis. We set DRAM cache and PMEM main memory to 4GB and 32 GB, respectively. We evaluate total 41 applications of 6 benchmark suites and compare PPA to the PMEM’s memory mode and our prior work Capri.

## Slide 21
Run-time Overheads (Lower is Better)
CPU2006
CPU2017
Normalized
Overhead
SPLASH3
All gmean
26%
Capri; HPDC’22
PPA
13%
1%
12%
0%
34%
2%
* Baseline is running original application on PMEM’s memory mode without crash consistency support
4%
63%
WSHIPER
17%
0%
STAMP
2%
Mini Apps
35%
1%
Notes: This figure shows the normalized performance overheads of PPA and Capri to the baseline. Here the baseline is running original program on PMEM’s memory mode. We can see from the figure, PPA outperforms Capri for all benchmarks. In summary, [click] PPA can lower Capri’s overhead from its 26% to only 2% [click]

## Slide 22
Region Characteristics
CPU2006
CPU2017
# Instructions
Per Regions
SPLASH3
All gmean
207
466
447
WHISPER
STAMP
319
Mini Apps
66
501
274
Notes: This figure shows the average region size across 6 benchmark suites. Thanks to the abundant free physical registers, PPA forms sufficiently long regions, [click] 319 instructions in each region on average. In this way, PPA has enough room to keep the core pipeline busy while performing asynchronous store persistence.

## Slide 23
Stall Cycles at Region End
CPU2006
CPU2017
# Stall Cycles
at Region End
SPLASH3
All gmean
0.8%
0.4%
0.2%
0.1%
WHISPER
STAMP
0.2%
Mini Apps
1.8%
0.1%
Notes: To showcase why PPA incurs such a low overhead. We compute the average ratio of the stall cycles occurred at the end of each region to the execution cycles of that region. As shown in the figure, PPA increases the stall cycle ratio of the baseline (PMEM’s memory mode) by [click] only 0.2% on average thanks to the long enough regions.

## Slide 24
The first lightweight/performant
microarchitectural approach
to WSP
Comparable performance
to PMEM’s memory mode
(no consistency support) with
negligible hardware costs and
energy consumption
Conclusion
ARF
NVM Main Memory
DRAM Cache
L2
L3
L1
Notes: In conclusion, PPA is the first lightweight yet high-performance microarchitectural approach to WSP. PPA achieves comparable performance to the PMEM’s memory mode with negligible hardware costs and energy consumption. [click]