## Slide 1
Soft Error Resilience at Near-Zero Cost
Jianping Zeng1, Shao-Yu Huang1, Jiuyang Liu2, Changhee Jung1
1. CompArch Lab, Purdue University, USA
2. Huazhong University of Science and Technology, China
Notes: Hello, this is Jianping Zeng from Purdue. I am going to present our paper VeriPipe: soft error resilience at near-zero cost.

## Slide 2
Soft Error and Its Increasing Concern
Notes: Soft errors are also known as transient faults which lead to bit flips. they are caused by high energy particle striking on the silicon. Unfortunately, the soft error rate goes up as technology shrinks.

## Slide 3
Sudden acceleration of a 2005 Camry in a September 2007 accident that killed one woman and seriously injured another
Single Bit Flip That Killed
https://www.eetimes.com/toyota-case-single-bit-flip-that-killed/
Notes: Even thought soft error just flips the bits, it could result in deadly damage, e.g., people suspected the bit flip caused the crash of a Toyota vehicle and killed one passenger in 2007. The key point is that soft error resilience is so critical that people came up with a lot of soft error detection techniques.

## Slide 4
Acoustic-Sensor-Based Soft Error Detection
Acoustic Sensor [ISCA’12, ISCA’14]
  Low Cost (< 1% area overhead)
  Bounded Worst-Case Detection Latency (WCDL)
Acoustic Sensor
WCDL
Notes: Among them, acoustic sensor-based error detection is particularly promising to detect soft errors in a low-cost manner, [click] incurring < 1% area cost of the chip. [click] It deploys a number of sensors on top of chip. When [click] a high energy particle hits the chip, [click] it always generates the sound wave as a result which can be perceived by the deployed sensors. In this way, there is no error missed. [click] Because of the propagation delay between striking location and sensor location, [click] it takes some cycles, [click] so called worst-case detection latency (WCDL), to sense the soft error. Based on this sensor based error detection, it is possible to achieve soft error verification. [click]

## Slide 5
Program Data Verification within WCDL
T1
T2
Time
Execution till T1 is error-free?
WCDL
Verified to be
error-free!
Notes: Soft error verification is to make sure if a program execution is error-free. The idea is very simple, here, we want to know if the execution prior to t1 is error-free, we just need to wait for WCDL cycles till T2. If no error has been detected within WCDL cycles, then the execution before T1 is ensured to be error-free. Otherwise, an error must have been already detected within the cycles, which indicates the execution prior to T1 has been corrupted. Based on this soft error verification, we can achieve error containment by only releasing verified data, let’s see how the state-of-the-art work achieves core-level error containment [click]

## Slide 6
Turnstile [MICRO’16]: Core-Level Error Containment
SQ
SQ
GSQ
* GSQ: Gated Store Queue
* ECC: Error-Correcting Code
Notes: To contain error in the core without corrupting the data in ECC-protected memory, [click] Turnstile repurposes the Store Queue in the core as gated store queue, GSQ such that Turnstile can control the release of the entries in the GSQ without releasing any unverified data to the cache. [click] In this way, no error escapes from core to the cache. Let’s see how turnstile works. [click]

## Slide 7
Store [A]
Store [B]
…
Store [C]
…
Store [A]
Store [B]
…
…
Store [C]
Rg1
Rg2
Time
t1
A
B
t1
Rg1
t2
t2
Rg2
C
WCDL
t3
WCDL
t4
A
B
Turnstile [MICRO’16]: Verifying Memory States
GSQ
C
A
B
A
B
* GSQ: Gated Store Queue.
* RBB: Region Boundary Buffer.
* Gray boxes are newly proposed
by Turnstile.
RBB
Rg2
Verified
Rg1
Recovery PC
Store verification allows memory verification
How to verify the register state?
Notes: Since GSQ is limited, turnstile achieves core level error containment at the region-level by [click] partitioning program [click] into a series of regions with GSQ size in mind. So that the number of stores in each region is not greater than the GSQ size. [click] During the execution of region 1, turnstile allocates a RBB entry for the region boundary, and [click] GSQ buffers the unverified stores of region 1. Likewise, [click] Turnstile allocates a RBB entry for region 2 and [click] buffers its stores in the GSQ. [click] suppose an error happens in region 2, which will be detected later. [click] At time t3, region 1 is verified to be error-free after spending WCDL cycles since the end of region 1. Therefore, [click] those stores of region 1, here, store A and B, can be safely released to the memory. Here, the PC of the last instruction of region 1 is copied to recovery PC in case a soft error occurs in the following region. [click] At time t4, [click] acoustic sensor detects the occurrence of the soft error, Turnstile [click] squashes unverified stores from the GSQ, such as store C of unverified region 2. After that, [click] Turnstile runtime resumes the program execution from the end of region 1 which is a recovery point. [click] in this way which we call store verification, turnstile can verify the memory state as part of program status. [click] The remaining question is how Turnstile verifies the register state which is also part of program status? [click]

## Slide 8
r2 = …
r3 (dead) = …
… = r1
… = r2
r3 = …
Rg2
Rg3
r1 = …
Rg1
r1 = ldr [ckpt_r1]
r2 = ldr [ckpt_r2]
Corrupted
Live-out
ckpt r2
ckpt r1
Live-out
Verified
Verified
Eagerly checkpoint registers after their most recently definitions in regions.
Checkpoint is essentially a store.
Turn register verification into memory verification
Run-time overhead due to eager checkpointing.
Over-complex hardware support.
Turnstile [MICRO’16]: Verifying Register States
Notes: To verify register status, [click] turnstile compiler identifies the live-out registers in each region, here, r1 in the region 1 and r2 in the region 2 because they are used in following region 3. [click] Then Turnstile compiler checkpoints those live out registers with [click] a checkpoint store after their definitions. In this way, [click] Turnstile turns the register verification into memory verification. We assume [click] region 1 and [click] region 2 are both verified, [click] and a soft error is detected in region 3. Turnstile only needs to rollback to the last verified region boundary. Remember that the memory state remains the same as all the stores after the last verified region are squashed. The checkpointed register state in the memory also remain intact because we turn register verification into memory verification. [click] Before rolling back to the last verified region boundary, [click] turnstile needs to first recover the register states by reloading checkpointed register values, here., r1 and r2, from checkpoint storage in the memory. [click] Then we can go back to the last verified region boundary for recovery. However, [click] Turnstile incurs a non-trivial run-time overhead due to eager checkpointing and [click] requires over-complex hardware support. To see what the fundamental reason is [click]

## Slide 9
New Viewpoint of Turnstile Region Verification
WCDL
t1
Region terminates
Start
Commit
(Verified)
Verify
(Timer
=WCDL)
Timer Expires
Execute
Timer is not zero
t2
t3
Rg1
Rg2
Rg3
Rg4
* Rg1 is under verification.
Time
Imprecise compiler analyses generate many short regions.
RBB overflows frequently, causing the core pipeline to stall due to structure hazard.
Notes: We propose a 3-stage verification pipeline to model Turnstile’s region verification. Suppose 4 regions in this example and Rg1 is being verified. Here, all regions are shorter than WCDL. [click] Once the core pipeline starts executing Rg1 at time t1, the verification pipeline enters into Execute stage. [click] Once the region execution finishes at time t2, the verification pipeline moves to Verify stage. At this point, [click] Turnstile sets a countdown timer to WCDL cycles and waits it to be zero. After spending WCDL cycles since the end of Rg1, [click] the verification pipeline moves to Commit stage at t3, [click] indicating Rg1 is now verified to be error-free if no acoustic error alarms the occurrence of soft errors. However, [click] imprecise compiler analyses generate many short regions. Therefore, region boundary buffer overflows frequently, leading to frequent core pipeline stalls due to structure hazard. To address this issue [click]

## Slide 10
VeriPipe: Near-Zero-Cost Region Verification Regardless of Long WCDL
Performance Overhead
VeriPipe
Turnstile [MICRO’16]
Expensive
Slow
Ideal
Turnpike [MICRO’21]
Notes: we propose VeriPipe , a near-zero cost region verification that incurs an average of only 1% run-time overhead while requiring 3 registers and 1 countdown timer no matter how long WCDL is. [click] As we have seen before, Turnstile is costly and incurs high run-time overhead. [click] Another approach is called Turnpike that uses hardware techniques to bypass verification for certain stores. However, Turnpike still incurs a moderate run-time overhead despite its even more complex hardware support. [click] Our novel microarchitecture technique enables VeriPipe to verify regions with way simpler hardware and a near-zero run-time overhead. Now, let’s talk about how VeriPipe works [click].

## Slide 11
VeriPipe Solution: Verifying Region at the Following Region End
WCDL
t1
Region terminates
Start
Commit
(Verified)
Verify
Next Region
Ends
Execute
t2
t3
Rg1
Rg2
Rg3
* Rg1 is under verification.
Time
Notes: We found out that Turnstile’s verification pipeline can be significantly simplified if a region is always verified to be error free at the end of the following region. Here, Rg1 is under verification, and all these regions are long enough to cover WCDL. In this example, [click] Rg1 starts with Execute stage at t1, and [click] then moves to Verify stage at time t2. Eventually, [click] Rg1 reaches Commit stage at t3 if there is no soft error detected before t3, [click] being verified to be error-free. Now, let’s see how to implement this simple verification pipeline. [click]

## Slide 12: Implementation of VeriPipe’s Verification Pipeline
time
Rg2
Rg3
t2
t3
Rg1
Recovery PC
Region Register
Rg2 verification pipeline
* Rg1 is under verification.
Recovery PC points to the end of latest verified region serving as a recovery point.
Region Register points to the end of the region being verified.
GSQ Ptr delineates unverified stores that must be squashed from GSQ in case of soft errors detected.
Rg1 verification pipeline
t1
Region Register
Recovery with unverified stores squashed from GSQ
Notes: To implement this simple verification pipeline, we propose 3 registers: [click] Recovery PC, [click] region register, and [click] GSQ Ptr. Recovery PC points to the end of the latest verified region, region register points to the end of the region being verified. GSQ pointer points to the end of the gated store queue when the core pipeline commits a region boundary instruction. Therefore, any stores younger than the GSQ pointer must be squashed in case of soft errors detected. In this example, Rg1 is being verified. [click] When the last instruction of Rg1 is committed at t2, [click] region register is updated with the PC of Rg1’s last instruction. Later, [click] at t3, Rg1 is verified to be error-free, [click] this is the point recovery PC is updated with region register. In addition, [click] region register is updated with the PC of the last instruction of Rg2. [click] In case of a soft error detected in Rg3, [click] VeriPipe runtime squashes all the unverified stores younger than the GSQ pointer and rolls back the program control to the end of Rg1 to resume program execution. In this way, VeriPipe always verifies regions at the end of the following regions. Unfortunately, it is not always possible to do so [click]

## Slide 13
Challenge of Verifying Region at the Following Region End
time
Rg2
WCDL
Rg1
Rg1 verification pipeline
t1
Rg3
t2
t3
* Rg1 is under verification.
Rg1’s Stores are
not verified yet
Corrupted stores
escape to the memory
Notes: This is because not every region is long enough to cover WCDL. Let’s see an example. Here, first two regions Rg1 and Rg2 are shorter than WCDL. As usual, Rg1 starts with Execute stage at time t1 and moves to verify at t2. Finally, Rg1 reaches commit stage at t3. However, [click] it is not safe to release Rg1’s stores to the cache because WCDL cycles haven’t been passed since the end of region 1. [click] What if a soft error occurs in Rg1, the corrupted data could escape to the cache, [click] compromising soft error resilience guarantee. To address this issue [click]

## Slide 14
Naïve Dynamic Region Enforcement: High Run-Time Overhead
time
Rg2
WCDL
Rg1
Rg1 verification pipeline
t1
Rg3
t2
t4
t3
Stalls
* Rg1 is under verification.
A global countdown timer tracks the elapsed cycles since the beginning of each region.
High run-time overhead caused by pipeline stalls, which increases as WCDL becomes longer.
Notes: one simple way is to stall the core pipeline at end of each short region. For this purpose, [click] we propose a countdown timer to track the cycles elapsed since the beginning of a region. [click] the timer sets to WCDL upon committing a region boundary instruction, for example at time t2. [click] at t3, rather than committing the region boundary instruction, [click] the core pipeline is stalled as the timer is not zero. [click] When the timer becomes zero at time t4, this is the point region 1 is verified to be error-free if no soft error is detected yet. [click] However, this naïve approach incurs too much performance overhead, and this overhead goes up as WCDL becomes longer. To address this challenge [click]

## Slide 15
VeriPipe Solution: Dynamic Region Stitching
Dynamically stitch a short region with prior regions such that the combined region is long enough to cover WCDL.
Still hold stores in the GSQ while enabling the region stitching.
time
Rg2
WCDL
Rg1
Rg1 verification pipeline
t1
Rg3
t2
t4
t3
* Rg1 is under verification.
NOP
No additional storage overhead, i.e., only a logic gate.
Maintain low run-time overhead for arbitrarily long WCDL.
Safe to release
stores from GSQ
Notes: [click] We propose a novel microarchitecture technique called dynamic region stitching that dynamically combines a short region with prior regions, ensuring the resulting region is long enough to cover WCDL. Also, we still hold the stores of the region being verified in the gated store queue to ensure correctness. [click] Now, let’s look at the same example to see how the region stitching works. At t2, the timer is set to WCDL and Rg1 starts its verification. [click] at t3, rather than stalling the core pipeline, [click] VeriPipe treats the region boundary instruction as a nop and continues executing the following instructions. Upon committing a region boundary, VeriPipe checks if the timer hits zero. [click] Here, at t4, the timer reaches zero and therefore [click] Rg1 is verified to be error-free, meaning that its stores can be safely released to the cache. [click] The beauty of this approach is that VeriPipe incurs no additional storage overhead and always maintains the low run-time overhead no matter how long the WCDL is. To improve the performance of the region stitching [click]

## Slide 16: Earlier Releasing Stores from GSQ Upon Zeroed-Out Timer
time
Rg2
WCDL
Rg1
Rg1 verification pipeline
t1
Rg3
t2
t4
t3
* Rg1 is under verification.
NOP
Safe to release
verified stores
Notes: We can earlier release stores to the cache when the timer hits zero. In this example, rather than waiting for the end of region 2, [click] we can directly release the stores of region 1 at time t4 since the timer already reaches zero at this point. As a result, [click] we achieve a high-performance region stitching without compromising soft error resilience guarantee. To further reduce the run-time overhead [click]

## Slide 17
Eliminating Redundant Checkpoints by VeriPipe Compiler Optimizations
#1: Speculative Loop Unrolling
#2: Loop Induction Variable Merging (LIVM)
r1 = …
ckpt r1
r2 = …
ckpt r2
...
r1 = …
ckpt r1
r2 = …
ckpt r2
...
… = r2
r1 = …
ckpt r1
r2 = …
ckpt r2
...
… = r2
#1
#2-4
#3: Loop Invariant Checkpoint Motion (LICM)
#4: Checkpoint Pruning
Rg1
Rg2
* #1 is from Capri; HPDC’22, while #2-4 are from Turnpike; MICRO’21
… = r2
Notes: VeriPipe leverages 3 existing compiler techniques to eliminate a lot of redundant checkpoint stores. First, [click] we use speculative loop unrolling from Capri to enlarge region size so that [click] certain checkpoints become redundant and thus can be removed, for example checkpoint r2 in region 1. In addition, [click] we use other 3 techniques from our prior work Turnpike to eliminate some of the remaining checkpoints without compromising soft error resilience guarantee, [click] for example, checkpoint r1 is removed from region 1.

## Slide 18
VeriPipe compiler partitions input program into recoverable and verifiable regions with GSQ size in mind.
VeriPipe hardware verifies them at the end of the following regions.
Recovery protocol
RECAP
VeriPipe
Compiler
…
r0 = Load [r2]
ckpt r0
…
Store r2, [r3]
…
Store r2, [r3]
…
…
r0 = Load [r2]
ckpt r0
…
Verifiable/Recoverable
Regions
Notes: So far, we talk about how VeriPipe verifies regions to be error-free when program is running. [click] Now, let’s see how to resume an error-interrupted program.

## Slide 19
Recovery Protocol
1c: ckpt r1;
2c: ckpt r2;
3: if (r1>r2)
4: r3 = r2*2;
4c: ckpt r3;
5: r3 = 0;
5c: ckpt r3;
Live in:r1,r2,r3
Rg2
r1 = ld [1c];
r2 = ld [2c];
r3 = r1>r2?
r2*2 : 0;
jmp [Rg3’s entry]
Recovery Block
Rg1
Rg3
Removed by checkpoint pruning
Squash SQ entries after Rg2’s end;
Runtime
* Rg1/Rg2 are already verified to be error-free.
Recovery
Point
Notes: In this example, [click] checkpoint 4c and 5c are eliminated by pruning. [click] region 1 and region 2 have already been verified such that the end of region 2 serves as a recovery point. Here, [click] suppose an error occurs in region 3. To recover the error-interrupted region 3, we should restore its live-in registers. For this reason, we let compiler generate a per-region recovery block that recovers region 3’s live in registers r1, r2, and r3. Here, [click] after squashing unverified stores from GSQ, [click] the recovery block reloads r1 and r2 from memory, while reconstructing r3 using recovered register r1 and r2, and constant values. After that, the runtime resumes the program execution from the beginning of region 3. Now, let’s see the evaluation and performance numbers [click]

## Slide 20
Gem5 Simulator
Clang/LLVM 13 and Benchmarks
Comparing Schemes
  Turnstile [MICRO’16] with RBB size 20
  VeriPipe [This Work]
Processor Core | 8-core, Out-of-Order, 2.42GHz, ARMv8 Cortex A77 running on Ubuntu 14.04 with Linux kernel 4.18.0
L1I & L1D Cache | Private, 64KB, 4-way, 4 cycle
L2 Cache | Private, 512KB, 8-way, 9 cycle
L3 Cache | Shared, 4MB, 16-way, 31-cycles
DRAM Cache | 16GB DDR4 2400 8x8
Evaluation
CPU2006 | CPU2017 | NPB C++ | SPLASH3 | Mini-apps
Notes: We implement VeriPipe hardware and compiler techniques on gem5 simulator and LLVM compiler, respectively. We model an 8-core ARMv8 cortex a77 processor and evaluate total 37 applications from 5 benchmark suites for Turnstile and VeriPipe. [click]

## Slide 21
Run-time Overhead (Lower is Better)
9% (up to 21%)
1%
5%
Turnstile
+ VeriPipe Compiler
+ Region Stitching (VeriPipe)
Normalized
Overhead
* WCDL defaults to 30 cycles.
* Baseline is running the original applications on the original hardware platform without soft error resilience guarantee.
Notes: This figure shows the normalized run-time overheads of 3 schemes to the baseline. Here, the baseline is running original applications on the original hardware without soft error resilience guarantee. We can see from this figure, Turnstile incurs an average of 9% and an up to 21% run-time overhead, while VeriPipe compiler can lower the run-time overhead to 5%. With dynamic region stitching, VeriPipe can further low the run-time overhead to only 1% no matter how long WCDL is.

## Slide 22
Hardware Cost Analysis (Lower is Better)
 | Area () | Power (mW) | Max. Access Latency (ns)
VeriPipe | 849.1 | 2.4 | 0.07
Turnstile | 9667.3 | 27.5 | 0.26
VeriPipe/Turnstile | 8.8% | 8.7% | 26.9%
 |  | Power (mW) | Max. Access Latency (ns)
VeriPipe | 849.1 | 2.4 | 0.07
Turnstile | 9667.3 | 27.5 | 0.26
VeriPipe/Turnstile | 8.8% | 8.7% | 26.9%
* Implemented using Chisel and a RTL compiler supporting 22nm technology.
Maximum of 3.86GHz clock frequency
Notes: To showcase how lightweight VeriPipe’s hardware is. We implement our hardware and Turnstile’s hardware using Chisel and evaluate their hardware overheads with an open-source RTL compiler which supports 22 nm technology. [click] This table shows that VeriPipe incurs only 9% hardware overhead of Turnstile. More importantly, [click] VeriPipe’s hardware has a maximum of 0.07 nano second access latency, while Turnstile’s is 0.26 nanoseconds, [click] which indicates the maximal clock frequency of turnstile-enabled processors is 3.86GHz.

## Slide 23
VeriPipe is the first near-zero (1%) run-time overhead for out-of-order cores no matter how long the WCDL is.
VeriPipe compiler generates less checkpoint stores.
VeriPipe incurs a minimal storage overhead, i.e., only 3 registers and 1 countdown timer, making the acoustic-sensor-based soft error resilience practical than ever for real silicon implementation.
Conclusion
Notes: In conclusion, VeriPipe is the first near-zero run-time overhead solution for out-of-order processors no matter how long the WCDL is. In addition, VeriPipe compiler generates less checkpoint stores. Moreover, VeriPipe minimizes the storage overhead to only 3 registers and 1 countdown timer, making acoustic-sensor-based soft error resilience practical than ever for real silicon implementation. This is all for my talk. Thank you so much for your listening. I am happy to take any questions.

## Slide 24
Backup Slides

## Slide 25
Run-time Overhead Breakdown (Lower is Better)
8%
1%
3%
3%
Naïve Region Enforcement
+LICM
Region Stitching
+ Unrolling (VeriPipe)
Normalized
Overhead
2%
1%
+LIVM
+Pruning
* WCDL defaults to 30 cycles.
* Baseline is running the original applications on the original hardware platform without soft error resilience guarantee.
Notes: To further investigate the benefit of each VeriPipe optimization, we break down the run-time overhead as shown in this figure. We can see that the naïve region enforcement incurs a high run-time overhead, while our region stitching can significantly lower the overhead to only 3%. Especially with VeriPipe compiler techniques, the run-time overhead is reduced to only 1%.

## Slide 26
Ratio of Stitched Regions (Higher is Better)
57%
51%
42%
47%
CPU2006
NPB
CPU2017
48%
49%
SPLASH3
Mini-apps
All geomean
Notes: To showcase why region stitching is so effective. We collect the ratio of the number of stitched regions to the total number of regions. This figure shows that the region stitching can eliminate 49% of regions on average, implying the minimal stall cycles occurred at the end of each region.